Pixy Cam Validation Check Sheet
Andrew Bryant

Milestone 3 – Testing the back end software

- Using a text file of fake Pixy Cam data, ensure the data is correctly being interpreted

[ ] 1) Read fake raw Pixy Cam data from text file
*Confirm the data is being read correctly (data assigned to correct rover / playing field marker)

[ ] 2) Translate data to two dimensional playing field representation
*Confirm the algorithm is working correctly to adjust for viewing angle
*Confirm map is correctly being read by comparing data with test text file

[ ] 3) Confirm the rover locations are being correctly assigned to the closest node
*Using raw data points from text file, ensure the adjusted x, y value is correctly
*Ensure the adjusted x, y value of each rover raw data is assigned the correct closest node value

[ ] 4) Ensure the Pacman rover is marked captured if within threshold distance
*Several raw data points will be close enough to where the rover should be marked captured
*Check output to ensure the captured value is True.

Milestone 4 – Testing the Pixy Cam data

- With actual playing field set up, place rovers around the field and check that the Pixy Cam is reading the field and interpreting the information correctly

[ ] 4) Confirm Pixy Cam is finding the actual playing field
*Place Pixy Cam in its mount above playing field
*Compare expected tile map of field with the tile map the Pixy Cam’s data is used to create

[ ] 5) Confirm Pixy Cam is finding rovers on field correctly
*Place rovers in various locations around the field, check output signals correct node
*If rovers are placed within threshold distance, check captured output value is True