Team 18 – Block Diagram

Andrew Bryant, Danny Dutton, Benjamin Singleton, John Spataro

PACMAN Rover
- SparkFun Line Following Sensor
  - Unidirectional data (sensor to PIC)
  - 8-bit data, corresponding to sensor eye state
  - I2C Interface
- ChipKit Motor Shield
  - GPIO speed and direction, 4-wire, unidirectional (PIC to shield), digital
  - I2C monitor, unidirectional byte (shield to PIC)
  - Servo motor out, 5-wire, PWM
- WiFly
  - Bidirectional serial asynchronous (UART)
  - Serial framed protocol (SOF, DATA, CHK, EOF)

GHOST Rover
Same I/O complement PACMAN Rover

PIXYCAM Driver
- PixyCam
  - Unidirectional I2C
  - Data contains location of sensed objects
- WiFly
  - Bidirectional serial asynchronous (UART)
  - Serial framed protocol (SOF, DATA, CHK, EOF)

PROCESSOR
- WiFly
  - Bidirectional serial asynchronous (UART)
  - Serial framed protocol (SOF, DATA, CHK, EOF)

RASPBERRY PI
- Wireless Dongle
  - Bidirectional, TCP/IP Wifi access point
- Software
  - Linux OS, Server Routing Software, Statistics and Debugging Monitor

LAPTOP
SSH Client